## Slide 1
Atmosphere to Electrons (A2e)
Aeroacoustics and Propagation
DOE Wind and Water Power Technologies Office
Patrick Moriarty
February 2014

## Slide 2: Overview
Why is aeroacoustics a thrust area?
  Noise is an impediment to wind energy construction
    Issue will grow as penetration levels increase
    No common understanding of what’s annoying
  Potential reductions in cost of energy
    Noise reduced operation is lost energy
    Some studies show increased tip speeds (i.e. noise) reduce turbine cost

## Slide 3: Correlation with A2e objectives
Optimized Performance of Existing Wind Plants
  LCOE Reduction
Seamless Grid Integration at High Penetration
  Reduce annual curtailment
Next Generation Wind Plant Technology Development
  Reduced acoustic emissions 6 dB relative to 105 dB baseline

## Slide 4: Approach for Strategy Development
Initial strategy document – November 2013
  Disseminated to experts and gathered initial feedback
Experts Meeting
  January 20-21, 2014 in Arlington, VA – day and half
  ~30 attendees (90 invitees)
  Breakout groups
    Turbine Technology
    Wind Plant Layout and Operation
    Community Impact
  Summary report by March
A2e Merit Review – February 2014
Planning group – subset of 6 experts
  Take expert meeting summary as input
  5-7 year plan to DOE by June

## Slide 5
Name | Organization | Industry Role
Pat Moriarty (Lead) | NREL | National Lab
David Maniaci | Sandia | National Lab
Matt Barone | Sandia | National Lab
Shreyas Ananthan | DOE WWPTO | DOE
William Devenport | Virginia Tech | Academic R&D
Kevin Kinzie | GE Wind | OEM
Mark Bastasch | CH2MHill | Acoustic Consultant
Key Contributors to Date

## Slide 6: Thrust Focus Areas
Turbine Technology
  Prediction and measurement of source
  Turbine design and control strategies
Wind Plant Layout and Operation
  Propagation
  Layout and operation
Community Impact
  Information vetting
  Public perception – what’s annoying?
  Measurement standards

## Slide 7: Current State of the Art
Turbine Technology
  Semi-empirical 2D noise models
  Wind tunnel testing common
  Serrations
  2-4% loss in AEP per 1 dB reduction
Wind Plant Layout and Operation
  Layout constraint on noise
  Simple propagation models – ISO 9613
  No interaction with…
    Terrain and vegetation
    Atmosphere
    Between turbines
Community Impact
  Varying community regulations
  Mis/disinformation prevalent
  No standard measurement or modeling practices
  Amplitude modulation thought to be most annoying

## Slide 8: Key Research Challenges and Technical Barriers
Turbine Technology
  Reduce noise at same power or
  Increase power with same noise
  Unsteady noise production
  Scaling
  Noise control
Wind Plant Layout and Operation
  Accurate and validated noise propagation models
    Terrain, vegetation and atmosphere
  Amplitude modulation physics
  How does turbine noise change within wind plants?
  Building/structural response
Community Impact
  Complaints from projects that meet regulation
  Determination of relevant metrics
  Extreme events may dominate instead of constant dB level
  Mis/disinformation
  Guidelines for regulation, modeling and measurement

## Slide 9: Approach
Technology Transfer
  Open source freely available datasets and simulation tools
  Open source geometries and control if possible
  IEA Task on Wind Plant Noise
Turbine Technology Goal
  -6 dB at constant power by 2020 relative to 105 dBA fleet average
Testing
  Airfoils, turbines and wind plants
  Wind tunnel
    Unsteady airfoil testing
  Sub and full scale
    Details of multiple turbines and inflow
    Range of operating and atmospheric conditions
    Topography
    Background noise

## Slide 10: Approach (cont.)
Propagation Studies
  Partnerships – NOAA, DoT, DoD, NASA
  Leverage previous research
  Range of atmospheric conditions
  Buildings/Structures
Amplitude Modulation
  Fundamental understanding of creation and propagation
Simulation Tools
  Turbines and wind plants including propagation
  Physically appropriate – time and spatially dependent
  Range of fidelity and quantify uncertainty bounds
  Periodic validation comparison exercises
Active and passive turbine and wind plant control

## Slide 11: Approach (cont.)
Human Response
  Partnerships - NASA and NIH
  Relevant metrics for wind turbine noise
    Probabilistic vs. deterministic
    Extremes vs. steady operation
  Infrasound detection
  Sleep studies
  Indoor/Outdoor sound transmission
  Dose response
Public Dissemination
  Website with continually updated information on wind turbine noise
    Comparison between 1980’s and now
    Review regulatory history for other sources
    Guidelines and best practices
      Modeling and measurements
      Review and update standards

## Slide 12: Accomplishment Expectations
Scientific understanding of annoyance and appropriate metrics
Independent objective summaries to inform wider community
Standards for wind turbine noise measurement and simulation
Propagation models for siting that include atmosphere, topography, and turbine interactions
Validated simulation tools with quantified uncertainty bounds
Tools and data for wind plant noise mitigation and control

## Slide 13: Timeline
2015
2016
2017
2018
2019
2020
Website for public
dissemination with
myths and facts
State of the art
summaries
Wind tunnel
airfoil testing
Full scale wind
plant test
Human Response
Studies
Model Validation
Exercise
Measurement and
modeling
guidelines
Propagation Model
Release
Begin IEA
Task
HFM Turbine
Model Release
Engineering Simulation
Tools Released
Wind Plant Control
Studies
Model Validation
Exercise

## Slide 14
DOE Program to Address Noise Issues:
  Combination of engineering and human response research
  Multiyear program of observations and modeling
  First priorities
    Information dissemination
    Propagation
    Human response
    Amplitude modulation
    Leverage outside expertise
Focus Questions for the Merit Panel:
  Proposed activities relevant?
  Highest priorities correct?
  Appropriate line between industry and DOE activities?
Summary

## Slide 15: Questions?