## Slide 1
Overview of DOE funded activities
Patrick Moriarty, Dave Maniaci, Matt Barone
January 20, 2014

## Slide 2: Example DOE Project
Eastern United States
Complaints from 12 homes (6 frequently) - 1000 homes within 3 km radius
The annoyance was described as an intermittent "thumping" sound
A "feeling" or "presence" was described… accompanied by sensations of uneasiness and personal disturbance.
Annoyance intermittent when turbines were running
Slower rotor reduced, but not eliminated annoyance
Not atypical reaction to problem wind project today

## Slide 3: Early History - 1980
MOD-1 turbine, Boone, North Carolina
  aka “Thumper”
  61 m rotor – 2 MW, GE-NASA Design
  Noise focused by terrain and atmosphere +25 dB in some locations
Different than today
  Downwind blade tower interaction
  High levels of infrasound and low frequency sound – resonance with building frequencies
  Airfoils often operating near stall
  Noise worse inside than outside
  Predecessor – MOD-0 100 kw – noise below ambient

## Slide 4: Building Amplification

## Slide 5: Low frequency/Infrasound

## Slide 6: Fast forward to 2013…
The Australian, July 24, 2013
  “MODERN wind turbines could cause the same health impacts for nearby residents as an older prototype rejected by the industry because of proven concerns, says the author of a 1987 study that established the link.”
Wind Turbine Syndrome blog, Nina Pierpont, July 6, 2013
  “U.S. government has known about Wind Turbine Syndrome since 1987…It’s now 2013, and the government and industry are still pretending they don’t know about this…”

## Slide 7: DOE Research 2002-2013
Small Wind
  Wind Tunnel Testing of Airfoils – NLR
Utility Scale Wind
  Virginia Tech
CFD/CAA Noise Modeling
  Penn State University
  Florida State University
Semi-Empirical Noise Modeling
  Began with Brooks, Pope and Marcolini (1989)
  Work with Franco Guidati
  NAFNoise and noise module within FAST
  Last update July 2005
Acoustic Array Development and measurements – two versions
Small studies
  Noise mitigation of blades
  Wind plant propagation
Research activities significantly curtailed in 2007 and stopped in 2014
Community Impact
  Small effort – mostly hearing concerns through WPA
  IEA Task 28 Social Acceptance of Wind Energy Projects
IEC standards testing and measurement standards development ongoing

## Slide 8: Small Wind Airfoil Testing
Wind tunnel testing
  Airfoils
  Tip shapes

## Slide 9: Tip Shape
Modify interaction of tip vortex with blade

## Slide 10: Utility Scale Wind Tunnel Testing

## Slide 11: Aeroacoustic Modeling
Semi-empirical methods
  Basic
Computational physics
  CFD-CAA
  Depends on accurate aerodynamic estimates
  Not completed according to original plan
Propagation Models
  Very basic

## Slide 12: Semi Empirical Code Validation
58 m downwind, d = 3°

## Slide 13: CAA Efforts
Acoustic Spectrum for S809 Airfoil at 30 deg Incidence
Acoustic spectrum at 3 observer locations (0 deg.-upstream; 45 deg; and 90 deg – overhead) 10 chords from an S809 airfoil at 30 deg. incidence, chord = 12 inches; span = 24 inches.
(a)
(b)
(c)
(a)
(b)
(c)
Preliminary

## Slide 14: Blade Shape
Spread out blade loading change through tower shadow
Computer fans

## Slide 15: Acoustic Array v 1.0
Acoustic array development and field measurements
  32 microphone array
  Deployed at NWTC and Sandia Bushland site
  Tests on Northwind 100-B and Micon BSDS blades
Validation of modeling tools with acoustic measurements
Notes: Noise is a big deal: constrains the entire design of the turbine, and a major siting barrier in some cases
Before noise can be mitigated, it must first be understood; to be understood, it must be measured in detail in the field

## Slide 16: Acoustic Array v 1.0
Field measurements using acoustic array and model comparison
Differentiation of individual blade noise and gearbox noise
Master’s thesis at University of Colorado and EWEC paper
Notes: - Highlight the ability to identify noise source locations on the blade

## Slide 17: NREL Acoustic Array v 2.0
64 microphones
Logarithmic spiral
Higher signal to noise
More weather resistant
Easily transportable

## Slide 18: Turbine Interactions

## Slide 19: Large Eddy Simulation of Trailing Edge
GE-Stanford-Sandia – usage of DOE HPC facilities

## Slide 20: Annoyance

## Slide 21: Amplitude Modulation
One theory why wind turbine noise more annoying than other common sources
Di Napoli, 2011

## Slide 22: Low Frequency Noise and Infrasound

## Slide 23: Wind Plant Noise Footprint